## Slide 1: Power Management Solutions for ULP SoCs Deliberate Practice – Session 2
Seyi and Aatmesh
1st May 2013

## Slide 2
Ultra Low Power SoCs ( e.g. BSN)
BSNs promise to change the way we live
Need higher life-time for ubiquitous deployment
Energy harvesting and Power Management is critical
Notes: Ultra Low Power Systems such as body sensor nodes promise to change the way we live. These systems provide rich information about activity, well being and environment. In this illustration BSNs are used to gather vitals of a subject continuously. It can alert a remotely located doctor in case of medical emergency. These systems are small in size and are often remotely located therefore need to have longer lifetime. Changing their batteries often is not possible, so they need to operate from harvested energy. Energy autonomy is central to their wide spread deployment

## Slide 3
Power Distribution in BSN
Efficient energy-harvesting ( E-harvesting)
  To increase the amount of harvested energy
Efficient multiple regulated output voltages
  To minimize the loss in voltage regulation
Power Management critical to BSN lifetime
Y. Zhang, et al, "A Batteryless 19uW…. ", JSSC, Jan. 2013.
19µW out of 50µW from TEG
Notes: This work focusses on the infrastructure circuits for the SoC. It needs efficient energy harvesting to increase the amount of harvested energy. Multiple regulated output voltages with higher efficiency to minimize loss and ultra-low power clocking to increase the lifetime in the idle mode.

## Slide 4
Power Supply Needs
Optimal energy point exists for each blocks such as CPU, Analog, RF etc.
Multiple regulated output voltages is needed.
A. Wang, et al, “A 180-mV Subthreshold …” JSSC, Jan. 2005
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 5
Power Supply needs for BSN
Optimal voltages exists for each Block in a BSN, which needs multiple supplies for BSN
Since BSNs operate in energy constrained environment each supply should be efficient
BSNs need efficient energy harvesting to further extend the lifetime
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 6
Limitation of existing solution
LDO
I
I
  Input power to the IC
    VDD*I
  Power taken from the source
    Vin*I
  Ideal Efficiency is given by,
    VDD*I/Vin*I=VDD/Vin
  Ex, Vin=1.2V and VDD=0.5V
  Efficiency is 0.41 or ~40%.
  Almost 60% of power is lost in regulation

## Slide 7
State of the art BSN SoC Power Management
Boost converter harvests the energy on to a capacitor at 1.35V
Multiple rails are served by linear regulators
63% 23% and 12% energy is lost in voltage regulation.
Y. Zhang, et al, "A Batteryless 19uW…. ", JSSC, Jan. 2013.

## Slide 8
Research Questions
There is a theoretical limit on the efficiency of LDO.
What can replace LDOs ??

## Slide 9
State of the art BSN SoC Power Management
Boost converter harvests the energy on to a capacitor at 1.35V
Multiple rails are served by linear regulators
63% 23% and 12% energy is lost in voltage regulation.
Y. Zhang, et al, "A Batteryless 19uW…. ", JSSC, Jan. 2013.

## Slide 10
Research Questions
BSN needs multiple output voltages.
How do solutions replacing LDOs can address this problem?

## Slide 11: Energy Harvesting
State of the art solution is 38% efficient.
How can we raise this efficiency?
Y. Zhang, et al, "A Batteryless 19uW…. ", ISSCC, Feb. 2012.

## Slide 12
Research Questions
How do voltage regulation and energy harvesting solutions integrate together for BSNs?
What additional costs are attributed to the solution?
How will the power of the new solutions be monitored?
e.g. DPM ( Shaksheer et. al.)